## Slide 1
AXI4-LITE INTRODUCTION
A simple control interface in Arm’s AMBA 4 family
01
Origin
Part of the AMBA specifications developed and published by Arm.
02
Release
AXI4-Lite appeared in AMBA 4 Phase One, announced in March 2010.
03
Purpose
Connects a CPU/host to control and status registers inside an IP block.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.
Repared by: Phạm Chí Đạt – Đinh Khánh Đăng

## Slide 2
AXI4-Lite
2/11
From AMBA to AXI4-Lite
AMBA
Advanced Microcontroller Bus Architecture: a family of on-chip SoC interface protocols.
2003
AMBA 3 introduced AXI, later commonly referred to as AXI3.
Mar 2010
Arm announced AMBA 4 Phase One, including AXI4, AXI4-Lite, and AXI4-Stream.
AXI4-Lite
A lightweight AXI4 branch for control registers, reducing protocol and wiring complexity.
Key idea: AXI4-Lite is not a high-throughput data bus. It is the standard “control path” used by software to configure IP, read status, and control operation.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 3
AXI4-Lite
3/11
What is AXI4-Lite?
Simple definition
• Memory-mapped protocol: the CPU accesses an IP block through register addresses.
• Each transaction transfers one data beat; long bursts are not used.
• Data is commonly 32-bit or 64-bit; WSTRB selects active write bytes.
• Best for CONTROL, STATUS, DATA, IRQ, and configuration registers.
Example register map
0x00 CONTROL start, reset, enable
0x04 STATUS done, busy, error
0x08 DATA_IN input word
0x0C DATA_OUT output word
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 4
AXI4-Lite
4/11
When should you use it?
Use AXI4-Lite for
• IP/peripheral configuration registers.
• Start/stop controls, software reset, function enable.
• Status flags: busy, done, error, interrupt pending.
• Small, occasional transfers without high-throughput requirements.
Avoid AXI4-Lite for
• Large continuous payload transfers requiring high bandwidth.
• Memory interfaces that need long bursts or many outstanding transactions.
• Video, audio, packet streams, or DMA data paths.
• Large buffers are better served by full AXI4, AXI4-Stream, or DMA.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 5
AXI4-Lite
5/11
VALID/READY handshake
Core rule
A transfer completes on a rising clock edge when VALID = 1 and READY = 1 on the same channel.
SOURCE
CPU / IP sends
DESTINATION
IP / CPU accepts
VALID: “I have information”
READY: “I can accept it”
• The source holds VALID until the handshake succeeds.
• The destination may deassert READY to apply back-pressure.
• If either signal is 0, address/data waits for a later cycle.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 6
AXI4-Lite
6/11
Five independent AXI4-Lite channels
AW
Write Address
where to write
W
Write Data
data + WSTRB
B
Write Response
write status
AR
Read Address
where to read
R
Read Data
data + RRESP
A write transaction uses 3 channels: AW carries address, W carries data, and B returns write status.
A read transaction uses 2 channels: AR carries the read address, and R returns data plus read status.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 7
AXI4-Lite
7/11
Write transaction: three channels
AXI4-Lite
Manager
Interface
AXI4-Lite
Subordinate
Interface
Write Address Channel
AWADDR, AWVALID, AWPROT
AWREADY
Write Data Channel
WDATA, WSTRB, WVALID
WREADY
Write Response Channel
BREADY
BRESP, BVALID
A write is complete only after the address, data, and write response handshakes have completed.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 8
AXI4-Lite
8/11
Read transaction: two channels
AXI4-Lite
Manager
Interface
AXI4-Lite
Subordinate
Interface
Read Address Channel
ARADDR, ARVALID, ARPROT
ARREADY
Read Data Channel
RREADY
RDATA, RRESP, RVALID
Compared with write transactions, reads are simpler because the response status travels with the R channel.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 9
AXI4-Lite
9/11
Main signal groups of the five channels
Channel
Main signals
Write address channel
AWVALID, AWREADY, AWADDR, AWPROT
Write data channel
WVALID, WREADY, WDATA, WSTRB
Write response channel
BVALID, BREADY, BRESP
Read address channel
ARVALID, ARREADY, ARADDR, ARPROT
Read data channel
RVALID, RREADY, RDATA, RRESP
Fast reading rule: use the prefix AW, W, B, AR, or R to identify the channel; use VALID/READY to identify the handshake signals.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 10
AXI4-Lite
10/11
RTL implementation tips
01
Define register map first
Specify address, read/write permission, reset value, and bit meaning before coding AXI logic.
02
Clean address decode
For 32-bit registers, low address bits are usually ignored because accesses are word-aligned.
03
WSTRB and byte writes
Update each byte according to WSTRB so software can modify selected byte lanes.
04
Correct responses
BRESP/RRESP usually return OKAY for valid accesses; signal errors when the system requires it.
05
Reset and back-pressure
Reset registers and VALID signals to safe values; READY may be 0 when a transfer cannot be accepted.
06
Verification
Test every register, delayed handshakes, reset during transfers, and WSTRB combinations.
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.

## Slide 11
AXI4-Lite
11/11
References
1
Arm — AMBA 4 / AMBA 3 / AMBA 2
https://www.arm.com/architecture/system-architectures/amba/amba-4
2
Arm — AMBA Specifications
https://www.arm.com/architecture/system-architectures/amba/amba-specifications
3
CIOL — ARM announces AMBA-4 phase one, 10 Mar 2010
https://www.ciol.com/arm-announces-amba-phase/
4
AMD — AMBA® AXI4 Interface Protocol
https://www.amd.com/en/products/adaptive-socs-and-fpgas/intellectual-property/axi.html
5
Real Digital — AXI4-Lite Interface tutorial
https://www.realdigital.org/doc/a9fee931f7a172423e1ba73f66ca4081
19 July 2026
Copyrights 2026 UIT. All Rights Reserved.