## Slide 1
PORTFOLIO
Copyrights 2026 CE-UIT. All Rights Reserved.
Verification of AXI4-Lite Based ALU IP
Đinh Khánh Đăng - Phạm Chí Đạt
IC VERIFICATION

## Slide 3
KHOA KỸ THUẬT MÁY TÍNH
Simplified Control Interface via AXI4-Lite
AXI4-Lite provides a simplified, non-burst interface ideal for memory-mapped control.
Protocol Selection & Efficiency
Selected for its high efficiency in handling memory-mapped control and status register (CSR) interfaces.
Compared to the AXI Full protocol, it eliminates complex burst transaction overhead.
Perfectly suited for lightweight, single-beat control mechanisms.
CPU
Master
Single-Beat
AXI4-Lite
CSR
Registers
Hardware-Software Control
Creates a highly reliable hardware-software link for system control.
Software writes configurations, operands, and triggers execution start signals.
Software seamlessly reads back hardware execution status and final computation results.
Software
(CPU Code)
Writes: Operands, Opcodes, Start
Reads: Status, Computation Results
Hardware
(CSR Registers)
Copyrights 2026 CE-UIT. All Rights Reserved.

## Slide 4
KHOA KỸ THUẬT MÁY TÍNH
Copyrights 2026 CE-UIT. All Rights Reserved.
Design Under Test (DUT) Architecture
Integrating five distinct sub-modules for execution and control
avalon_axi4lite_alu
Avalon Bus
INTERFACE & CONTROL
avalon_axi4lite_ bridge
Avalon to AXI4-Lite
axi4lite_slave
AXI Protocol Decoder
EXECUTION & STORAGE
axi_register_bank
Config & Operands
alu_core
Arithmetic & Logic
avalon_axi4lite_alu
The top-level wrapper integrating all sub-modules into a cohesive unit.
avalon_axi4lite_bridge
Adapts incoming Avalon bus transactions to the AXI4-Lite protocol standard.
axi4lite_slave
Decodes AXI protocol handshakes and manages register read/write access.
axi_register_bank
Stores operational configuration, input operands, and output results.
alu_core
Executes the core arithmetic and logic operations.

## Slide 5
KHOA KỸ THUẬT MÁY TÍNH
Register Map Interface Bridge
A strictly defined register map bridges the software firmware flow to the RTL design.
Control & Status
0x00 CTRL
Control register for start and reset signals.
0x04 STATUS
Status register indicating busy, done, or error states.
Data Input
0x08 Operand A
32-bit input operand A.
0x0C Operand B
32-bit input operand B.
Operation Config
0x10 Opcode
Selector for the specific arithmetic or logic operation.
Execution Results
0x14 Result
The final ALU computation output.
Copyrights 2026 CE-UIT. All Rights Reserved.

## Slide 6
KHOA KỸ THUẬT MÁY TÍNH
AXI4-Lite Handshake & Stall Compliance
Verification ensures strict protocol compliance across independent channel handshakes
Write Channel Protocol
■ Out-of-Order Arrival: Verifies independent handshake performance and correct out-of-order arrival of Write Address (AW) and Write Data (W).
■ Internal Write Enable: Monitors internal write enables to ensure they pulse for exactly one cycle only when both AW and W handshakes complete.
■ BVALID Stall Rules: Verifies BVALID remains high until BREADY is asserted, guaranteeing correct handshake response and proper channel stall handling.
Read Channel Protocol
■ AR Handshake Check: Ensures proper Read Address (AR) handshakes are executed cleanly as the first stage of any read transaction.
■ RVALID/RDATA Delay: Verifies proper sequence and checks the correct delay relationship between the AR handshake and subsequent RVALID/RDATA output.
■ Response Validation: Evaluates and validates read transaction data responses directly against the established OKAY standard.
Copyrights 2026 CE-UIT. All Rights Reserved.

## Slide 7
KHOA KỸ THUẬT MÁY TÍNH
A Multi-Tiered Verification Strategy
Ensures robust functional and protocol coverage.
01
Directed Testing
Targets specific functional corner cases and basic bring-up scenarios.
02
Constrained Random
Generates randomized operands, addresses, byte enables, and bus stall conditions to find unexpected edge cases.
03
Assertions (ABV)
Utilizes SystemVerilog Assertions (SVA) to continuously monitor protocol handshakes.
04
Scoreboard Model
Employs a reference predictor model (C/Python or SystemVerilog) to automatically verify ALU outputs against expected golden results.
Copyrights 2026 CE-UIT. All Rights Reserved.

## Slide 8
KHOA KỸ THUẬT MÁY TÍNH
Robust Stimulus Matrix for Dual-Core IP Verification
Targeting out-of-order transactions, handshake stalls, and invalid address accesses
axi4lite_slave Test Suite
Transaction Ordering: Stressing AW arriving before W, W arriving before AW, and simultaneous arrivals.
Interface Stalls: Injecting randomized BVALID and RVALID stalls to challenge interface robustness.
Back-to-Back Operations: Verifying back-to-back read and write transaction sequences under load.
axi_register_bank Test Suite
Register Access: Validating basic write and read access behavior for operands and opcodes.
Byte Masking: Verifying byte enable masking functionality on partial register writes.
Handshake Protocols: Triggering start pulses while monitoring busy, done, and error states.
Invalid Accesses: Actively executing out-of-bounds and invalid address accesses to ensure proper error recovery.
Copyrights 2026 CE-UIT. All Rights Reserved.

## Slide 9
KHOA KỸ THUẬT MÁY TÍNH
Comprehensive Functional Coverage Plan
Tracks operational states, transaction stalls, and critical protocol crosses
Opcode Coverpoints
Instruction Types
■ADD / SUB: Standard math
■MUL / DIV: Complex math
Illegal Instructions
■Invalid: Error handling
Operand & Byte Enables
Operand Classes
■Zero / One: Boundary inputs
■Max / Random: Extreme ranges
Byte Enables
■0000 / 1111: Null and full writes
■Single / Mixed: Partial strobe
Protocol & Stall Types
Write Ordering
■AW / W First: Phase skew timing
■Simultaneous: Concurrent phases
Stall Types
■B/R Channel Stalls: Backpressure
■Handshake Delay: Dynamic stalls
Critical Cross Coverage
Cross Relations
■Opcode × Error: Exception modes
■Address × Byte En: Alignment cases
■Write Order × Stall: Phase delay sync
Verification Goal
■Ensure complex, deep corner cases are validated
Copyrights 2026 CE-UIT. All Rights Reserved.

## Slide 10
KHOA KỸ THUẬT MÁY TÍNH
Copyrights 2026 CE-UIT. All Rights Reserved.
The DUT strictly writes to registers only when both
address and data handshakes complete.
Example Write Handshake Waveform (W before AW)
W Handshake
AW Handshake
Register Write
T0
T1
T2
T3
T4
T5
CLK
AWVALID
AWREADY
WVALID
WREADY
wr_en
BVALID
BREADY
AXI Protocol Compliance
The waveform highlights critical signals: AWVALID, AWREADY, WVALID, WREADY, internal wr_en, BVALID, and BREADY.
In this scenario, the write data (W) is presented first, but the internal write enable (wr_en) does not assert until the write address (AW) handshake also successfully completes.
This prevents premature write transactions and ensures robust data compliance with AMBA AXI protocols.

## Slide 11
KHOA KỸ THUẬT MÁY TÍNH
Core Block-Level Verification Status
Primary core blocks executed and passing; top-level integration pending
Block-Level Achievements
All primary block-level testbenches successfully executed and passing.
High initial functional and structural coverage reached on ALU and AXI slave modules.
98.5%
Code
Coverage
95.0%
Toggle
Coverage
856
Passing Tests
Open Integration & Closure Items
Formal Assertion Checks
Complete all pending formal assertion checks to mathematically verify core interfaces.
Coverage Closure Reports
Generate and review final structural and functional coverage closure reports.
Extended Random Stress Testing
Extend simulated testing run times and stress parameters to uncover corner cases.
Top-Level Nios II Verification
Integrate all blocks and execute verification via the software compiler runtime.
Copyrights 2026 CE-UIT. All Rights Reserved.

## Slide 12
KHOA KỸ THUẬT MÁY TÍNH
Mastering Protocol Specifications for
Robust Hardware Verification
01
Protocol Spec Mastery
Interpreting standard specifications and defining block-level verification partitions to establish secure IP interface boundaries.
02
Control Flow Mapping
Mapping software control flows directly to hardware execution behavior, particularly around critical handshake and stall corner cases.
03
SVA & Coverage Closure
Deploying comprehensive SVA protocol checkers to target dynamic failures and successfully closing remaining functional coverage gaps.
04
End-to-End System Flow
Scaling up constrained random stress testing to robustly verify and validate the end-to-end Avalon-to-AXI system interconnect flow.
Copyrights 2026 CE-UIT. All Rights Reserved.